## Slide 1: FNAL beam test results
A. Zhang, V. Bhopatkar, M. Phipps,
J. Twigger, M. Hohlmann
HEP Group A, Florida Tech
12/16/2013

## Slide 2
Beam profiles from reference detectors
Applied a coarse alignment: shift the reference detectors to the beam center by subtracting the mean value of the cluster position distribution.
1st ref. #2 (10cm)
2nd ref. #3 (10cm)
3rd ref. #4 (50cm)
4th ref. #1 (10cm, FIT)

## Slide 3
X,Y correlations of reference detectors
The correlation band from the upstream ref. detectors is quite narrow,
and the band becomes a little wider for the downstream ref. detectors.

## Slide 4
5 tracks
Z [mm]
Y [mm]
X [mm]
Some 3d tracks
The solid dots have same color are one track that goes through the four ref. detectors.
Most of the tracks have 3 points in a good line.

## Slide 5
Tracks in y-z plane
The same alignments are used to EIC ZZ and 10cm ZZ detectors.

## Slide 6
More tracks from ref. detectors
Cut: positions in y axis are between -1.0 and +1.0 mm
The beam size in X direction is ~30mm, much wider than ~1.5mm in Y. This is consistent with our previous results.
The beam is parallel in X-Z projection, while looks has angles in Y-Z projection.

## Slide 7
Residual distribution of EIC ZZ detector
3200V
The sigma is obviously decreasing as HV increases!

## Slide 8
Efficiency curve of EIC ZZ detector, on sector 5, with the coarse aligned tracking information.
Cut: clusters on ref. detectors have more than 1 strips, cluster on EIC eta5 has none-zero strip.
Get >97% efficiency when HV above 3200V.
Efficiency of EIC ZZ detector on sector 5

## Slide 9: Summary
The first tracking results look promising, though the alignment is coarse.
Will work on fine alignment to get more precise tracks
And spatial resolutions.
Thanks!